## Slide 1: Somacis ZZ PCB Results Contiued…
B.Azmoun, BNL

## Slide 2: Earlier results: Piece-wise linear correlation plots
Initial results: used APV25/SRS with low gain to avoid saturation, but effectively imposed a threshold cut on small amplitude hits

## Slide 3: Simulate high threshold for Centroid calc.
Initial Measurement: Piecewise linear with global slope of 1, but local slope of ~1/2
Charge distributed uniformly over three pads at a time
Charge distr. is linear wrt pos. on all pads
User input constraint: % of tot. charge on middle pad is a variable at pad center
Fixed constraint: 50/50 charge sharing at half-way point btwn pads
Continuous linearity is influenced by
Gain
Threshold
Saturation point
Degree of charge sharing
Under certain circumstances will get a fragmented linear correlation
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 0
Gain = 2
Sat. point = 100% of max signal
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 30
Gain = 2
Sat. point = 100% of max signal
Piece-wise slope ~1/2

## Slide 4
Motor Position (mm)
Q(pad)/Q(tot) (mm)
The measured charge ratio is also very similar to the simulated results
The jump in the charge ratio at 3, 5, and 7mm, (corresponding to the pad center -- see ZZ sketch on previous slide) from one pad to the next is due to the threshold cutoff and is responsible for the fragmented linear correlation
Saving Grace: by examining the ratio plots, we can determine the correction factor to regain a fully linear response, which in this case happens to be 2
Charge apparently discontinuously jumps from one pad to the next
If the cutoff is made = 0, the charge from one pad gradually goes to zero, while it simultaneously grows on the next and the fragmentation in the correlation is removed
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 30
Gain = 2
Sat. point = 100% of max signal
Same measurement
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 0
Gain = 2
Sat. point = 100% of max signal (No sat.)
Effective threshold

## Slide 5: New Measurements at higher Gain
Struck ADC w/ single ch. Hybrid PA + Shaper
=
Low hit threshold
+ high gain (~7500)
+ no saturation
s ~100mm
N/S ~1-3%
s ~70mm
N/S ~ 1-3%

## Slide 6: Summary: Old ZZ PCB Vs New ZZ PCB
Measured physical ZZ Parameters | p (mm) | d (mm) | s (mm) | g (mm) | Strip Overlap / Pitch (%) | Gap / Pitch (%) | Electrode Area / Tot. PCB Active Area (%) | Resoltiom w/ DNL (um) (no sngl pad hits) | Resoltiom w/o DNL (um) (no sngl pad hits) | % of Single pad hit Events
Old Design/PCB | 2.00 | 0.5 | 0.159 | 0.082 | 69.0 | 4.1 | 66.0 | 132 | 98 | ~30%
New Design/PCB | 2.00 | 0.586 | 0.141 | 0.084 | 82.5 | 4.2 | 63.0 | 100 | 70 | ~5%

## Slide 7: Perpendicular Scan
Charge ratio spectra at 5 points within a 500mm ZZ period
Min charge ~10%
Spectra at all five points have the same shape  uniform pad response across ZZ periods
Smallest charge for a fired pad is ~10% of total collected charge
By scanning perpendicularly, the uniformity of the pad response may be checked across the ZZ period

## Slide 8: Publications
Poster @ 2017 IEEE NSS/MIC
Conference proceedings being submitted this Friday
TNS paper to follow once we have beam test results with new PCB
(New PCB will allow us to scan the parameter space of a reasonable range ZZ parameters)

## Slide 9: Backup

## Slide 10
Bigger circle:
~75% charge on one pad at center
(for illustrative purposes only; circles are not to scale)
50/50 sharing point
Pad center: majority of charge on one pad (in this example: 90% or 75%)
Smaller circle:
~90% charge on one pad at center
Measurement: Piecewise linear with global slope of 1, but local slope of ~1/2
Charge distributed uniformly over three pads at a time
Charge distr. is linear wrt pos. on all pads
User input constraint: % of tot. charge on middle pad is a variable at pad center
Fixed constraint: 50/50 charge sharing at half-way point btwn pads
Continuous linearity is influenced by
Gain
Threshold
Saturation point
Degree of charge sharing
Under certain circumstances will get a fragmented linear correlation
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 0
Gain = 2
Sat. point = 100% of max signal
Simulation Parameters
Max % charge on single pad = 65%
Charge Amp. threshold Cut = 30
Gain = 2
Sat. point = 100% of max signal
Piece-wise slope ~1/2